## Slide 1: Computer Networks The Network Layer
Lecture 7
Adrian Sergiu DARABANT

## Slide 2: The Network Layer

## Slide 3: The Internet Protocol -IP
The Internet (IP) Protocol
  IPv4 addressing
  Moving a datagram from source to destination
  Datagram format
  IP fragmentation
  ICMP: Internet Control Message Protocol
  DHCP: Dynamic Host Configuration Protocol
  NAT: Network Address Translation
  Routing

## Slide 4: The Internet Network Layer
forwarding
table
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Link layer
physical layer
Network
layer

## Slide 5: IP Addressing
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host may have multiple interfaces
  IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 6: IP Addressing
IP address:
  network part (high order bits)
  host part (low order bits)
What’s a network ? (from IP address perspective)
  device interfaces with same network part of IP address
  can physically reach each other without intervening router=no crossroads
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
network consisting of 3 IP networks
(for IP addresses starting with 223,
first 24 bits are network address)
LAN

## Slide 7
IP Addressing
How to find the networks?
Detach each interface from router, host
create “islands of isolated networks
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
Interconnected
system consisting
of six networks

## Slide 8: IP Addresses – Class Full
0
network
host
10
network
host
110
network
host
1110
multicast address
A
B
C
D
class
1.0.0.0 to
127.255.255.255
128.0.0.0 to
191.255.255.255
192.0.0.0 to
223.255.255.255
224.0.0.0 to
239.255.255.255
32 bits
given the notion of “network”, let’s re-examine IP addresses:
“class-full” addressing:
1111
Experimental
E
240.0.0.0 to
255.255.255.255

## Slide 9: IP Addressing: CIDR
Classful addressing:
  inefficient use of address space, address space exhaustion
  e.g., class B net allocates enough addresses for 65K hosts, even if we only have 2K hosts in that network
CIDR: Classless InterDomain Routing
  network portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in network portion of address
11001000 00010111 00010000 00000000
network
part
host
part
200.23.16.0/23

## Slide 10: IP Subnet
Basic concept:
  A subset of a class A, B or C network.
IP addresses that do not use subnets consist of
  A network portion, and
  A host portion.
Represents a static two-level hierarchical addressing model.

## Slide 11: IP Subnet (cont)
IP subnets introduces a third level of hierarchy.
  A network portion
  A subnet portion
  A host portion
Allow more efficient (and structured) utilization of the addresses.
Uses network masks.
usually handled together as network
but with substructure

## Slide 12: CIDR – Introduction
The size of the global routing tables have grown very fast in recent years.
  Caused routers to become saturated.
CIDR is a new concept to manage IP networks.
  Classless Inter Domain Routing.
  No concept of class A, B, C networks.
  Reduces sizes of routing tables.

## Slide 13: CIDR - Basic Idea
An IP address is represented by a prefix, which is the IP address of the network.
It is followed by a slash, followed by a number M.
  M: number of leftmost contiguous bits to be used for the network mask.
  Example: 144.16.192.57 / 18

## Slide 14: CIDR - Rules
The number of addresses in each block must be a power of 2.
The beginning address in each block must be divisible by the number of addresses in the block.
  A block that contains 16 addresses cannot have beginning address as 193.226.40.36.
  But the address 193.226.40.64 is possible !

## Slide 15: IP/Netmask - examples
209.220.186.8/255.255.255.252=>
209.220.186.8
209.220.186.9
209.220.186.10
209.220.186.11
209.220.186.8/255.255.255.248=>
209.220.186.8
209.220.186.9
209.220.186.10
209.220.186.11
209.220.186.12
209.220.186.13
209.220.186.14
209.220.186.15
209.220.186.8/255.255.255.240
Invalid combination

## Slide 16: Network masks
Network mask 255.0.0.0 is applied to a class A network 10.0.0.0;
  Mask = series of contiguous 1’s followed by a series of contiguous 0’s
11111111 00000000 00000000 00000000
NETWORK
HOST

## Slide 17: Natural Masks
Provide a mechanism to split the IP address 10.0.0.20 into:
  A network portion – 10;
  A host portion – 0.0.20;
IP Address: 10.0.0.20 00001010 00000000 00000000 00010100
Mask: 255.0.0.0 11111111 00000000 00000000 00000000
Network Host

## Slide 18: Natural masks
Class A, B and C addresses
  Have fixed division of network and host portions
  Can be expressed as masks
Natural Masks
  Class A: 255.0.0.0
  Class B: 255.255.0.0
  Class C: 255.255.255.0

## Slide 19: Subnets out of masks
Masks are very flexible.
  Using masks, networks can be divided into smaller subnets.
How?
  By extending the network portion of the address into the host portion.
Advantage gained:
  We can create a large number of subnets from one network.
  Can have less number of hosts per network.

## Slide 20: Network Address
IP Address
193.226.40.45
AND
Network Address
193.226.40.0
Network Mask
255.255.255.0
IP Address
193.226.40.45
AND
Network Address
?
Network Mask
255.255.255.224
Network Address
193.226.40.32

## Slide 21: Subnetting
Basic concept
  The same network can be configured with different masks.
  Can have subnets of different sizes.
  Allows better utilization of available addresses.

## Slide 22: Example
Suppose we are assigned a Class C network 193.226.40.0
  To be divided into three subnets.
    Corresponding to three departments.
    With 110, 45 and 50 hosts respectively
D1
110
D2
45
D3
50

## Slide 23: Example (cont) - Options
X | X(binary) | # of Subnets | # of Hosts
128 | 1000 0000 | 2 | 128
192 | 1100 0000 | 4 | 64
224 | 1110 0000 | 8 | 32
240 | 1111 0000 | 16 | 16
248 | 1111 1000 | 32 | 8
252 | 1111 1100 | 64 | 4
254 | 1111 1110 | 128 | 2
Network too small
Rules:
First IP address = Network Address
Last IP address = Broadcast Address

## Slide 24: How does one get IP Addresses ?
Q: How does a network get the network part of IP addr?
A: it gets allocated from the portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 25: Supernetting
“Send me anything with addresses beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP
Organization 0
Organization 7
Internet
Organization 1
200.23.20.0/23
Organization 2
.
.
.
.
.
.
200.23.32.0/24
Organization 8
Multiple Routing entries become a single one !
200.23.16.0/20
?
?
200.23.32.0/24
Two routes
Supernetting aggregates routes !

## Slide 26: Reserved Addresses

## Slide 27: Private Addreses
Name | IP address range | number of IPs | classful description | largest CIDR block | defined in
24-bit block | 10.0.0.0 – 10.255.255.255 | 16,777,216 | single class A | 10.0.0.0/8 | RFC 1597 (obsolete), RFC 1918
20-bit block | 172.16.0.0 – 172.31.255.255 | 1,048,576 | 16 contiguous class Bs | 172.16.0.0/12 | 
16-bit block | 192.168.0.0 – 192.168.255.255 | 65,536 | 256 contiguous class Cs | 192.168.0.0/16 | 
Not routed in Internet
Why ?

## Slide 28: Routing tables (static)
Destination | Gateway | Genmask | Flags | Metric | Ref | Use | Iface
172.16.25.1 | 172.30.0.4 | 255.255.255.255 | UGH | 0 | 0 | 0 | Eth1
193.226.40.128 | 0.0.0.0 | 255.255.255.224 | U | 0 | 0 |  | Eth0
193.0.225.0 | 0.0.0.0 | 255.255.255.0 | U | 0 | 0 |  | 
193.231.20.0 | 0.0.0.0 | 255.255.255.0 | U | 0 | 0 |  | Eth0
172.30.0.0 | 0.0.0.0 | 255.255.0.0 | U | 0 | 0 |  | Eth1
169.254.0.0 | 0.0.0.0 | 255.255.0.0 | U | 0 | 0 |  | Eth1
0.0.0.0 | 193.0.225.9 | 0.0.0.0 | UG | 0 | 0 |  | Eth0
The route command – (Windows/Linux/other OS)

## Slide 29: Datagram: from source to destination
IP datagram:
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
misc
fields
source
IP addr
dest
IP addr
data
datagram remains unchanged, as it travels source to destination
Addresses are fields of interest here
forwarding table in A
Dest Net | Mask | Nxt Router | Metric
223.1.1.0 | 255.255.255.0 |  | 1
223.1.2.0 | 255.255.255.0 | 223.1.1.4 | 2
223.1.3.0 | 255.255.255.0 | 223.1.1.4 | 2
64.8.32.1 | 255.255.255.255 | 223.1.1.10 | 2

## Slide 30: Datagram: from source to destination
Starting at A, send IP datagram addressed to B:
look up net. address of B in forwarding table
find B is on same net. as A
link layer will send datagram directly to B inside link-layer frame
  B and A are directly connected
misc
fields
223.1.1.1
223.1.1.3
data
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
forwarding table in A
Dest Net | Mask | Nxt Router | Metric
223.1.1.0 | 255.255.255.0 |  | 1
223.1.2.0 | 255.255.255.0 | 223.1.1.4 | 2
223.1.3.0 | 255.255.255.0 | 223.1.1.4 | 2
64.8.32.1 | 255.255.255.255 | 223.1.1.10 | 2

## Slide 31: Datagram: from source to destination
Starting at A, dest. E:
look up network address of E in forwarding table
E on different network
  A, E not directly attached
routing table: next hop router to E is 223.1.1.4
link layer sends datagram to router 223.1.1.4 inside link-layer frame
datagram arrives at 223.1.1.4
continued…..
misc
fields
223.1.1.1
223.1.2.2
data
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
forwarding table in A
Dest Net | Mask | Nxt Router | Metric
223.1.1.0 | 255.255.255.0 |  | 1
223.1.2.0 | 255.255.255.0 | 223.1.1.4 | 2
223.1.3.0 | 255.255.255.0 | 223.1.1.4 | 2
64.8.32.1 | 255.255.255.255 | 223.1.1.10 | 2

## Slide 32: Datagram: from source to destination
Arriving at 223.1.4, destined for 223.1.2.2
look up network address of E in router’s forwarding table
E on same network as router’s interface 223.1.2.9
  router, E directly attached
link layer sends datagram to 223.1.2.2 inside link-layer frame via interface 223.1.2.9
datagram arrives at 223.1.2.2!!! (hooray!)
misc
fields
223.1.1.1
223.1.2.3
data
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
forwarding table in router
Dest Net | Mask | Nxt R | Metric | Interface
223.1.1.0 | 255.255.255.0 | - | 1 | 223.1.1.4
223.1.2.0 | 255.255.255.0 | - | 1 | 223.1.2.9
223.1.3.0 | 255.255.255.0 | - | 1 | 223.1.3.27